## Slide 1
Project 3 Pin Diagram
MSP430
Keypad
C2
C3
C4
R1
P5.3
P5.1
P5.0
P5.4
GND
VCC
5V
Led 1
P1.0
C1
P1.4
R2
P1.1
R3
P3.5
R4
P3.1
P6.1
P6.2
P6.3
P6.4
P6.0
P6.5
P1.5
P1.6
P1.7
3V3

## Slide 2
Init
Initialize LED 1 (Red) as output on P1.0
Initialize LED 2 (Green) as output on P6.6
Initialize Switch 1 as input with pull up on P2.3
Initialize Switch 2 as input with pull up on P4.1
Enable Software Reset
Setup I2C Clock, Master, and Slave
Setup I2C ports SDA = P1.2 SCL = P1.3
Setup UART Clock for 57600 baud and Tx
Setup UART ports P4.3 = UCATDX
Setup ADC on P5.0
Disable software reset
Enable Interrupts for switches, UART, and I2C
Take out of low power mode
Enable global interrupt
Main
Project 3 Flowchart - Main
Wrong
Change LED Pattern
Update RGB Status Led
Wait for passcode
Correct
Read Keypad
If D

## Slide 3
Project 3 System Architecture Diagram
RGB LED
KEYPAD
LED ARRAY
TIMER
PWM CONTROLLER
GPIO